## Slide 1
JARVIS — System Block Diagram
Voice-controlled embedded assistant — component and data-flow overview
ESP32-S3
Wake-word engine + command logic
Microphone
Analog audio in (MAX4466)
Button
Stop / dismiss
Wit.ai
Cloud speech intent API
MAX7219 Matrix
8x8 LED — heart display
SSD1306 OLED
Live status text
Audio Playback
DFPlayer Mini → TPA3116D2 → Speaker
Status LEDs
White (light) / Red (mood)
raw PCM audio
GPIO input
HTTPS POST audio / JSON intent
bit-banged SPI
I2C
UART command
GPIO
Microcontroller (hub)
On-device peripheral
Cloud service
data / control flow